## Slide 1: CMSIS – Pathway to ARM eco-system
    Consistent, generic, and standardized software building blocks
    Includes full featured RTOS kernel
    Available for all Cortex-M processors and Cortex-A5, A7, A9 processors
    Software Packs to distribute device support and software building blocks
    Open source – development public on github
Used in many projects > 1,200,000 source files public on GitHub
Device family packs
> 3,000,000 pack downloads
in past 6 months
4150 devices
supported with CMSIS
Q4’2016
CMSIS-Zone MPU Support RTX5 certification
5.2
5.0
5.1
CMSIS-RTOS2 RTX5 ARMv8-M Support
Support for
Cortex-A5, A7, A9
Q3’2017
Q1’2018
Released
Development
CMSIS Roadmap
Notes: The Cmsis (Cortex Microcontroller Software Interface Standard) standard is a collection of API definitions, libraries, utilities, and methods that simplify and accelerate the creation of microcontroller applications. Cmsis is provided FOC by ARM (and the contributors) with a permissive Apache 2.0 licenses and the software components can be used in any open source and commercial projects.
Users (software programmers) benefit from RTOS, DSP-Libraries, consistent access to peripheral, and debug visibility.
SiPs (device vendors) have a clear process to deploy support for new devices along with hardware abstraction layers and software libraries.
The device support is delivered in Device Family Packs (that typically support a complete family of [many] microcontrollers) and can be used with several main stream tools including ARM Keil MDK and the new DS-MDK.
CMSIS is supported by all leading toolchains and allows SiPs to focus on the creation of the device (not on establishing contacts with the members of large ARM Eco-System).
That is the reason for our headline: CMSIS – The Pathway to the ARM Eco-System!
For more information visit www.arm.com/cmsis

## Slide 2: Challenge of system partitioning
different power domain
Flash
Cortex-M33
SRAM Cntl
APB Bridge
Multi-layer AHB5 interconnect
System SRAM
Instruction Cache
TrustZone Cryptocell
IDAU
Always-on domain
TrustZone
Filters
TrustZone
Filters
Cortex-M33
Instruction Cache
IDAU
Local SRAM
TrustZone
Filters
Power
Control
TrustZone
Filters
Secure Debug
CoreSight SoC
QSPI
SPI
I3C
eMMC
GPIO
PWM
SDIO
master
UART
SDIO
slave
I2C
master
I2C
slave
I2S
USB2
RTC
Cortex-M23
Code RAM
IDAU
TCM
TrustZone
Filters
AHB5 interconnect
I2C
Async Domain Bridge
DMA
    Systems with multiple processors or multiple execution domains require consistent partitioning
      Configurations need to match hardware setup, memory allocation, and peripheral usage

## Slide 3: CMSIS-Zone – making system partitioning easy
Resource configuration for multi-processor systems and execution regions
System Resources
Project Zones
Execution Zones
Build
  List available system resources in multi-processor systems
  CMSIS-Zone development workflow
  Select resources for independent software projects
  Partition memory & peripherals for safe process execution
  Generate tool setup and
  hardware configuration

## Slide 4: CMSIS-Zone – making system partitioning easy
Resource configuration for multi-processor systems and execution regions
System Resources
  Collect available system resources of multi-processor systems
  CMSIS-Zone development workflow
Project Zones
  Select resources for independent software projects
Build
Execution Zones
  Partition memory and peripherals for safe process execution
Build
  Generate tool setup and hardware configuration

## Slide 5: XML Files
System Resources
  CMSIS-Zone development workflow
Project Zones
Build
Execution Zones
*.szone lists all available system resources and stores all project zone assignments in a central file.
*.pzone is project zone specific and lists only system resources and project zone assignments specific to a project zone (this file may be introduced later).
*.xzone stores assignments specific to a project zone. As input the *.szone or *.pzone file is used

## Slide 6: RTOS MPU extension – easy setup with CMSIS-Zone
Non-secure state
Secure state
Process A Thread A0, A1, A2
Process B Thread B0, B1
Memory Protection Unit for safe process/thread execution
Shared Interfaces
Process C Thread C0 … Cn
handler mode
thread mode
each box is MPU protected
RTX RTOS Kernel
Interrupt Handlers
thread mode
handler mode
each box is MPU protected
System Start
Secure Storage
Crypto Functions
Interrupt Handlers
TrustZone RTOS Context Management
Priority
Priority

## Slide 7: CMSIS-Zone – data export for projects
FreeMarker template engine allows to export CMSIS-Zone data
Build
  Flexible data export for project build supports many different use cases: i.e. device configuration, MPU setup, linker scripts, etc.
file templates
CMSIS-Zone data
FreeMarker
    Project files for:
    Memory assignments and linker configuration
    SAU, MPU configuration
    Peripheral assignments