## Slide 1: A Simplified ARMv8-M Use Case
I/O Driver
User Application
Non-secure state
Secure State
Firmware
Code
Const
Data
Function Calls
Function Calls
Function Calls
TrustZone enabled Microcontroller
Only Function Calls to Secure part are possible
Non-secure part cannot access Secure resources
Secure part may access everything
Secure and Non-secure parts may implement independent time scheduling
User Project
Firmware Project
Start
System Start
Communication Stack
Notes: For explaining the software for Trustzone-M let me start with a simplified use case diagram. The complete application is split into a firmware project – that executes in secure state – and a user project – that executes in non-secure state.
A TrustZone-M enabled microcontroller allows you to develop firmware that is access protected from the user application. The firmware publishes only certain API functions that are market with the SecureGate instruction. Only these functions can be called by the application. The user project has no direct access to firmware code and data or the hardware resources that are protected by the Security Attribute Unit.
For example a firmware project may provide a communication stack. And since the communication can be encrypted already in the communication stack you use I/O drivers that execute in non-secure state. This allows you to configure the I/O channel as needed for your application while benefiting from a standardized and temper resistant communication stack. The secure state provides also a completely independent SysTick timer which you may used to diagnose error conditions in the user application or the peripherals. The secure state has full access to the non-secure state which may be used to restart a crashed user application or bring it back into a safe operating mode.
A TrustZone-M enable microcontroller offers a whole new range for possibilities - designed to significantly improve applications that require security or safety or even both.

## Slide 2: ARMv8M Programmers Model – Memory Map
Non-secure memory view is identical with Cortex-M
Branches to fixed memory locations access Secure firmware
Secure memory is invisible
Non-Secure state
Flash
RAM
Peripherals
Off-chip memory
Off-chip peripherals
System Control and Debug
ROM Tables
0x00000000
0xFFFFFFFF
0xF0000000
0xE0000000
0xA0000000
0x60000000
0x40000000
0x20000000
Vector table for Non-secure handlers
ITM/DWT/FBP
SysTick
NVIC
SCB
MPU
Debug

## Slide 3: ARMv8M Programmers Model – Memory Map
Non-Secure Flash
Secure Flash
Non-secure RAM
Secure RAM
Non-secure peripherals
Secure peripherals
Off-chip memory
Off-chip peripherals
System Control and Debug
ROM Tables
ITM/DWT/FBP
Secure SysTick
NVIC
Secure SCB
Secure MPU
Secure Attribution Unit
Debug
Non-Secure SysTick Alias
Non-Secure SCB Alias
Non-Secure MPU Alias
Secure state
Vector table for Secure handlers
Secure memory view shows additional Flash, RAM, and Peripherals.
Access to all regions is possible in Secure state
Regions can be configured in Secure state using the Secure Attribution Unit
0x00000000
0xFFFFFFFF
0xF0000000
0xE0000000
0xA0000000
0x60000000
0x40000000
0x20000000

## Slide 4: ARMv8M Programmers Model – Register
Handler Mode
Thread Mode
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
SP (R13)
LR (R14)
PC (R15)
PSR
Non-secure state
Secure state
PSP_NS
PSPLIM_NS
MSP_NS
MSPLIM_NS
Handler Mode
Thread Mode
PSP_S
PSPLIM_S
MSP_S
MSPLIM_S
PRIMASK_NS
FAULTMASK_NS
BASEPRI_NS
PRIMASK_S
FAULTMASK_S
BASEPRI_S
CONTROL_NS
CONTROL_S
General purpose registers Visible in all states
Separate stacks for Secure and Non-secure state with hardware stack limit check
Non-secure access to interrupt control registers is configurable in Secure state

## Slide 5: CMSIS-CORE for Secure Mode Projects
startup_<compiler>.c CMSIS Device Startup
system_<device>.c
CMSIS System & Clock Configuration
<user>.c/c++ User Application main() { ... }
<device>.h CMSIS Device Peripheral Access
partition_<device>.h Secure Attributes & Interrupt Assignment
CMSIS-CORE Device Files
CMSIS-CORE Header Files generated from CMSIS-SVD
User Program
Files relating to CMSIS-CORE including device specific files
partitions.h provides initial setup for Secure Attribution Unit and configures Non Secure mode memory areas and interrupts