## Slide 1: CMSIS Version 3 adds CMSIS-RTOS – an API Interface Standard for 3rd party Real-Time Operating Systems

## Slide 2: Cortex Microcontroller Standard (CMSIS)
Abstraction layer for all Cortex-M processor based devices
    CMSIS-CORE : API for Cortex-M processor and core peripherals
    CMSIS-DSP : DSP Library with 61 functions for Cortex-M
    CMSIS-SVD : XML system view description for peripherals
    CMSIS-RTOS : API for RTOS integration
Benefits to the embedded developer
  Consistent software interfaces for silicon and middleware vendors
  Simplifies re-use across Cortex-M processor-based devices
  Reduces learning curve, development costs, and time-to-market
New
Notes: 2
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 3: CMSIS Version 3: Structure
Debugger (3rd Party)
USER
CMSIS
MCU
Cortex CPU
SysTick RTOS Kernel Timer
NVIC Nested Vectored Interrupt Controller
Debug + Trace
Other Peripherals
Device Peripheral Functions (Silicon Vendor)
SIMD Cortex-M4
Peripheral
View
CMSIS-
SVD
System View Description (XML)
Real Time Kernel (3rd Party)
CMSIS-RTOS
API
Application Code
Peripheral Register & Interrupt Vector Definitions
CMSIS-CORE
Core Peripheral Functions
CMSIS-DSP
DSP-Library

## Slide 4: CMSIS Version 3: Components
CMSIS-CORE: Standard API for all Cortex-M Processors
  Standardized interface for Cortex-M0, M3, M4 and future processors
  SIMD Intrinsic Functions for Cortex-M4 instruction enhancements
CMSIS-DSP: DSP Library Collection with 61 Functions
  Data types: Fixed (fractional q7, q15, q31) and Float-Point
  Optimized for Cortex-M4, but also available for Cortex-M0, M3
CMSIS-RTOS: Standard API for Real-Time OS Vendors
  Standardized Interface to Real-Time Operating Systems
  Enables Software Templates, Middleware, Libraries, etc.
CMSIS-SVD: System View Description for Peripherals
  Peripheral Awareness for Debuggers
  Header file generation for Peripheral Register + Interrupt Definitions
New
Notes: 4
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 5: CMSIS Version 3: Components
CMSIS-CORE: Standard API for all Cortex-M Processors
  Standardized interface for Cortex-M0, M3, M4 and future processors
  SIMD Intrinsic Functions for Cortex-M4 instruction enhancements
CMSIS-DSP: DSP Library Collection with 61 Functions
  Data types: Fixed (fractional q7, q15, q31) and Float-Point
  Optimized for Cortex-M4, but also available for Cortex-M0, M3
CMSIS-RTOS: Standard API for Real-Time OS Vendors
  Standardized Interface to Real-Time Operating Systems
  Enables Software Templates, Middleware, Libraries, etc.
CMSIS-SVD: System View Description for Peripherals
  Peripheral Awareness for Debuggers
  Header file generation for Peripheral Register + Interrupt Definitions
Notes: 5
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 6: CMSIS-CORE: Abstract
CMSIS-CORE provides a Peripheral Access Layer with
  Consistent layout of all peripheral registers
  Vector definitions for all exceptions and interrupts
  Functions to access core registers and core peripherals
  Debug channel (for printf-style + RTOS Kernel)
CMSIS-CORE compliant software components allow
  Easy reuse of example applications and template code
  Combination of software components from multiple vendors
The CMSIS-CORE enables deployment of software components to physical Microcontroller Devices

## Slide 7: What CMSIS-CORE is not(!)
CMSIS-CORE does not make Peripherals Equal
  Peripheral Access Layer defines common methods, not features
    I/O, Timers, PWM, A/D, D/A, etc. can function differently
CMSIS-CORE does not require immense Resources
  Peripheral Access Layer requires < 1KB code, 4Bytes variable.
    Including device startup code
CMSIS-CORE does not prevent from direct Hardware Access
  Peripheral Registers are accessed via memory accesses
    Each Peripheral has a struct that collects all registers
    Device documentation should reflect this structure
The CMSIS-CORE is not another complex software layer that forces vendors to unify features

## Slide 8: Files for CMSIS-CORE Layer
startup_<device>.s CMSIS Device Startup Interrupt Vectors
system_<device>.c CMSIS System & Clock Configuration
core_<cpu>.h CMSIS CPU & Core Access
system_<device>.h CMSIS System & Clock Configuration
cmsis_compiler.h Core Peripheral Functions CPU Instruction Access SIMD Instruction Access
<user>.c/c++ User Application main() { ... }
<device>.h CMSIS Device Peripheral Access
CMSIS-CORE Device Files (Silicon Vendor)
CMSIS-CORE Standard Files (ARM)
User Program
To use CMSIS in a project add:
  Startup_<device>.s: Compiler-specific startup code.
  System_<device>.c: System Configuration file
  <device>.h: Header file for device peripheral access
  <device> is represents the device name, i.e. STM32F4
Notes: 8

## Slide 9: Files for CMSIS-CORE Layer
startup_<device>.s CMSIS Device Startup Interrupt Vectors
system_<device>.c CMSIS System & Clock Configuration
<user>.c/c++ User Application main() { ... }
<device>.h CMSIS Device Peripheral Access
CMSIS-CORE Device Files (Silicon Vendor)
User Program
Notes: 9

## Slide 10: CMSIS Version 3: Components
CMSIS-CORE: Standard API for all Cortex-M Processors
  Standardized interface for Cortex-M0, M3, M4 and future processors
  SIMD Intrinsic Functions for Cortex-M4 instruction enhancements
CMSIS-DSP: DSP Library Collection with 61 Functions
  Data types: Fixed (fractional q7, q15, q31) and Float-Point
  Optimized for Cortex-M4, but also available for Cortex-M0, M3
CMSIS-RTOS: Standard API for Real-Time OS Vendors
  Standardized Interface to Real-Time Operating Systems
  Enables Software Templates, Middleware, Libraries, etc.
CMSIS-SVD: System View Description for Peripherals
  Peripheral Awareness for Debuggers
  Header file generation for Peripheral Register + Interrupt Definitions
Notes: 10
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 11: CMSIS-DSP Library
Collection of 61 algorithms
  C Source Code, optimized for Cortex-M0, Cortex-M3, and Cortex-M4
  For CMSIS compliant C Compilers (ARM/Keil, IAR, GCC)

## Slide 12: CMSIS-DSP Library
Extends application range of Cortex-M MCUs to high-performance, low power signal processing
    On Cortex-M4: optimized for SIMD and FPU instruction set
    Even Cortex-M0 variant of DSP library in CMSIS V2.1 (released)
Free of charge: as for all CMSIS components
    For silicon vendors, tool partners, and end-user’s
Generic, vendor independent, designed to be a standard
  Works with RTOS message/mail passing system (i.e. Keil RTX)
    But can be used stand-alone
  DSP Standard Library avoids lock-in with proprietary solutions
    Essential to stimulate design utilities and future middleware
    For CMSIS compliant C Compilers (ARM/Keil, IAR, GCC)

## Slide 13: DSP Library Performance
Cortex-M4 SIMD + FPU
  Fix point: ~2x faster
  Floating point: ~10x faster
2,244
8,819
FIR q15 fixed point
41
IIR q31 fixed point
8,596
PID q15 fixed point
8,310
Matrix Mul fixed point
13,619
158,878
Correlationfloating point
2,462
27
2,462
DSP Library Benchmark: Cortex-M3 vs. Cortex-M4
Cortex-M3
Cortex-M4
Memory Access Cycles
Cycles: smaller numbers are better
- 75%
- 35%
- 69%
- 70%
- 91%
On Cortex-M4: uses SIMD & FPU instructions

## Slide 14: CMSIS Version 3: Components
CMSIS-CORE: Standard API for all Cortex-M Processors
  Standardized interface for Cortex-M0, M3, M4 and future processors
  SIMD Intrinsic Functions for Cortex-M4 instruction enhancements
CMSIS-DSP: DSP Library Collection with 61 Functions
  Data types: Fixed (fractional q7, q15, q31) and Float-Point
  Optimized for Cortex-M4, but also available for Cortex-M0, M3
CMSIS-RTOS: Standard API for Real-Time OS Vendors
  Standardized Interface to Real-Time Operating Systems
  Enables Software Templates, Middleware, Libraries, etc.
CMSIS-SVD: System View Description for Peripherals
  Peripheral Awareness for Debuggers
  Header file generation for Peripheral Register + Interrupt Definitions
Notes: 14
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 15: CMSIS-RTOS API: Motivation
Provide a standardized API for software components
  Stimulate standard middleware development
  Provide platform for Java (JVM) or UML (both need an RTOS)
  Enable standard project templates from SiPs (i.e. motor control)
  Simplify usage of CMSIS-DSP Library
Simplify programming of Cortex-M based devices
  Provide SiPs and middleware industry with standard RTOS APIs
  Reduce learning curve for programmers
API designed with the vision for:
  MPU access protection and multi-processor systems
  Software eco system that allows application sharing (AppStore)
RTOS vendor competition will encourage optimization for Cortex-M
  Use Cortex-M processor features (LDEX, STEX, WFE, WFI)
  Use CoreSight for Kernel-aware debugging
Notes: 15

## Slide 16: CMSIS-RTOS: Minimum Requirements
Preemptive context switching with multiple priorities
Mutex, Semaphore, Event signal, and Time management
Message queue and Mail queue that works with interrupts
Optional features that allow differentiation:
Generic Wait function; i.e. with support of time intervals
Support of MPU
Zero-copy mail queue
  Support multi-processor systems; support for DMA controller
Deterministic context switching; round-robin context switching
  Dead look avoidance i.e. with priority inversion
No interrupt disable on Cortex-M3/M4
  Usage of Cortex-M3/M4 instructions (i.e. LDEX, STEX)
Suitable for all Cortex-M processor variants;
  Supported by all CMSIS Compiler and Debug vendors
Notes: 16

## Slide 17: CMSIS-RTOS: API Structure
Real Time Kernel (3rd Party)
Function call translation
Application Code
main thread interrupt
Object definition
via macros
CMSIS-RTOS API
Objects
API Design Considerations
  Suitable for all Cortex-M Processors
  Small memory foot print
  Scalable functionality
  Prepared for MPU support
  Prepared for multi-processor systems
Object Definition
  With type information that allows type checking and debug views
  Abstracted via macros to allow implementation specific internal data structures
API Functions and Function Call Translation
  Powerful, flexible API functions. Optional: ‘main’ starts as thread and functional groups.
  API calls possible from threads or interrupts; illegal calls form interrupts are rejected
  Converts CMSIS-RTOS API calls to 3rd party RTOS functions
  Kernel Objects only referenced by address; allows MPU protection
Notes: 17

## Slide 18: CMSIS-RTOS: Function Overview
$ optional functions
Notes: 18

## Slide 19: Files for CMSIS-RTOS Layer
startup_<device>.s CMSIS Device Startup Interrupt Vectors
system_<device>.c CMSIS System & Clock Configuration
<user>.c/c++ User Application main() { ... }
<device>.h CMSIS Device Peripheral Access
RTOS.LIB CMSIS Compliant RTOS Library
cmsis_os.h CMSIS Standard RTOS Interface
RTOS_config.c CMSIS RTOS Configuration
CMSIS-CORE Device Files (Silicon Vendor)
CMSIS-RTOS Standard Files (RTOS Vendor)
User Program
To use CMSIS-RTOS add:
  RTOS.LIB
  RTOS_config.c
  cmsis_os.h
Note: Files are RTOS specific
Notes: 19

## Slide 20: CMSIS-RTOS: Thread Management
Thread State Changes
Thread Definition
  Thread description defines: thread function, initial priority, stack size
  Thread ID created at thread starts; multiple thread instances possible
  Thread ID refer an active thread
  Pre-emptive context switching with seven easy to understand priorities: Idle, Low, BelowNormal, Normal, AboveNormal, High, Realtime
Thread Management
  Create: start a thread
  Terminate: stop a thread
  GetPriority: obtain current thread priority
  SetPrioirty: change priority of tread
  Thread ID specifies any active thread
  Thread ID = NULL allows to refer the current running thread
Notes: 20

## Slide 21: CMSIS-RTOS: Mutex & Semaphore
#0
shared resource
Resource Sharing
  Mutex: for thread only - for classic thread synchronization
  Semaphore: for thread - counting semaphore - binary semaphore (count = 1) - semaphores can be also released in ISR
Mutex: Synchronization
Semaphore: Shared Access
Semaphore
#1
#2
#3
#4
#5
Thread
Thread
Thread
Thread
wait release
wait release
wait release
wait release
shared resource
Mutex
Thread
Thread
wait release
wait release
Notes: 21

## Slide 22: CMSIS-RTOS: Message & Mail
Thread or ISR
Thread or ISR
put
get
Message Queue
int / pointer values
Thread or ISR
Thread or ISR
put
get
Mail Queue
memory blocks
. . . . . .
alloc
free
Message/Mail Queues
  Buffered information exchange between threads or interrupt service routines (ISR)
  Queue operations: - put info to queue (Thread, ISR) - get info from queue (Thread, ISR) - wait for info (Thread only)
  Suited for multi-processor architectures
  Memory blocks used for mail might be access protected via MPU
Message/Mail Description
  Contain data type for run-time type checking and kernel aware debugging
  Define queue size and optionally the receiving thread
Message: Integer or Pointer
Mail: Memory Blocks
Notes: 22

## Slide 23: CMSIS-RTOS: Time Management
Time
  A Timer Thread handles multiple Callback Functions
  One-Shot or periodic function callbacks can be started, restarted, or stopped
  The callback function has an argument and can use other RTOS API calls
  Timeout and Time Delay in each Thread
  osDelay suspends a thread for a specific time period.
  Functions that wait for a resource (semaphore, mail, mutex, etc.) support timeout value
Callback
Callback
Callback
Callback
osTimerStart
osTimerStart (restart timer)
osTimerStop
Notes: 23

## Slide 24: CMSIS-API: RTOS Potential
Source: EE Times Group - 2010 Embedded Market Study
Operating Systems (Kernels) for deeply embedded
(Cortex-M based MCU)
All have similar basic features
But no common API
Notes: 24

## Slide 25: CMSIS-RTOS: Making it a Success
CMSIS has already created a large community
  Cortex-M Processors are an Industry Standard MCU Platform
  Simplifies creation of new devices and tool support
RTOS API extends CMSIS to more complex software
  A strong statement to drive “standardization” in the industry
  But allows “superset” products with more functionality (MPU support, certification suites, etc.)
CMSIS-RTOS Reference Implementation based on RTX
  Free BSD license including source code: allows flexible usage & distribution
  Compatible with ARMCC, GCC Compilers, and IAR
mBED extended with CMSIS RTOS API
Available Implementations
Notes: 25

## Slide 26: CMSIS Version 3: Components
CMSIS-CORE: Standard API for all Cortex-M Processors
  Standardized interface for Cortex-M0, M3, M4 and future processors
  SIMD Intrinsic Functions for Cortex-M4 instruction enhancements
CMSIS-DSP: DSP Library Collection with 61 Functions
  Data types: Fixed (fractional q7, q15, q31) and Float-Point
  Optimized for Cortex-M4, but also available for Cortex-M0, M3
CMSIS-RTOS: Standard API for Real-Time OS Vendors
  Standardized Interface to Real-Time Operating Systems
  Enables Software Templates, Middleware, Libraries, etc.
CMSIS-SVD: System View Description for Peripherals
  Peripheral Awareness for Debuggers
  Header file generation for Peripheral Register + Interrupt Definitions
Notes: 26
For the benefit of the embedded developer
- Reduce Complexity
- Provide Industry-Wide Programming Standards
- Support Partnerships and Innovation

## Slide 27: CMSIS-SVD
Use Cases
  Device specific Peripheral Views in debugger
  Device header file generation
Scope
  One device or series per file, describing peripherals
  Peripherals contain the registers, registers contain bit-fields
  Address and bit position, naming and descriptions
XML based description format
  Defined by written specification and XML Schema
  Validated for semantic consistency (SVDConv)
Challenges
  Value of the solution depends on the level of detail
  Management of CMSIS-SVD files
Notes: Use Cases: header file generation was not within the original scope of the “System View Description” format, however a number of partners see high value in this capability and it seems we only need a bit of additional information to achieve this. This could bring high level of conformance checking
Challenges: silicon vendor need to provide detailed descriptions including meaningful descriptions on all levels, however tool-vendors need to be able to provide instant access to these details in their debugger

## Slide 28: CMSIS-SVD – Status
CMSIS-SVD Version 1.0
  stable since June 2010
Traction
  11 Silicon Vendors shipping
  8 Silicon Vendors work in progress
  400+ CMSIS-SVD files submitted
  At least 4 Tool Vendors supporting SVD for debugging
SVDConv Utility from ARM
  Checks XML descriptions for consistency
  Generates a CMSIS compliant device header file
  Generates input file for MDK-ARM System Viewer
Notes: Shipping: Atmel, Energy Micro, Freescale, Fujitsu, Holtek, Nuvoton, NXP, ST, TI, Toshiba
In progress: Analog Devices, Cypress, Infineon, MicroSemi, Nordic, Samsung, SiLabs, Sonix
Supporting Toolchains: Atollic, IAR, Keil, Rowley, Raisonnance
Signed Contract: Energy Micro
Contract in Review: Atmel, Freescale, ST, (NXP)
Pending ARM Legal: Fujitsu, Toshiba, TI,

## Slide 29: CMSIS-SVD Database
Web-based Management for Silicon Vendors
  Upload/Update of CMSIS-SVD files
    Includes Schema and Consistency Check
  Add/Edit Devices
    Define device name and associate SVD-File
    Access control through review permission and publishing date
  Review access provides access to an unpublished device

## Slide 30: SVD: Upload, Review, Publish
Owned by
Silicon Vendor
SVD
Storage
Checks
Passed?
Discard
Publish?
Reviewer?
Device
Database
Public
Download
Review
Access
https://cmsis.arm.com/user/index.php
www.arm.com/cmsis
Denied
EULA
accepted
Denied
SVD
File

## Slide 31
Thank You!
The CMSIS enables
  Consistent and simple software interfaces
  Simplified software reuse
  Shortened learning curve for microcontroller developers
  Reduced time to market for new devices